Project FORCE
FORCEMBLER Specification
Dominik Wezel
# Overview
The FORCEMBLER makes it possible to insert assembler code mnemonics directly into FORCE code.
## Mnemonic Notation
FORCEMBLER is a RPN assembler, i. e. the operands are coded before the operation code, and the operands themselves are generally in the order EXTRA SOURCE TARGET.
## Using the FORCEMBLER With FORCE
### Don’t Mix Wildly
It is generally regarded as bad practice (and a huge impediment for portability) to wildly mix assembler code into FORCE code. Instead, assembler code should be restricted to specially designed areas, and the module header should state that the module contains assembler code.
### MacroForcembler
To make assembler code more portable (at the cost of losing some flexibility), an additional layer called MacroForcembler has been coded, which interfaces between FORCE and assembler code. The MacroForcembler provides higher level words for primitive operations, without hiding the original Forcembler.
When porting FORCE to a different platform, writing the Forcembler and recoding the MacroForcembler will cover the big part. In a fully portable library, it is 100% of the porting process.
### Paradigm
In the rest of this manual, the IA64 Forcembler will serve as a paradigm.
### Enabling and Disabling the Forcembler
By default, the Forcembler is hidden inside the compiler. There are two ways to enable it:
- by importing it explicitly;
- by using the compiler words A[ for enabling and ]A for disabling it.